## Slide 1: Aviation safety & certification of new operations and systems
Dr.ir. L.J.P. (Lennaert) Speijker
NLR Air Transport Safety Institute
ASCOS User Group Workshop 2, 19/20 September 2013, JRC Ispra

## Slide 2: This presentation
Background
Scope
Main impacts and benefits
Project objectives
Relation between objectives
Phases
User Group interaction
Contact details

## Slide 3: Background
Many innovative technologies and operational concepts are not implemented due to issues arising with safety and certification
Many operators and users are eager to use new developments
To ease introduction of safety enhancement systems & operations, an innovative approach towards certification is required that:
  Is more flexible with regard to the introduction of new products and operations;
  Is more efficient, in terms of cost, time & safety, than current certification processes;
  Considers safety impact of all aviation system elements and the entire system life-cycle in a complete integrated way.

## Slide 4: Scope
Proposed operational/system changes in total aviation system
Proposed changes should enhance safety of operational issues
Commercial Air Transport
Contribution to reaching the ACARE Vision 2020 safety goals
Time frame (specifying how far ASCOS looks into the future) for actual introduction of proposed changes is around 2020
Application of proposed certification process adaptations, to be delivered by ASCOS, assuming take up by the authorities

## Slide 5: Main impact and benefits
ASCOS is necessary to remove undue certification obstacles and enable implementation of technologies to reach ACARE & Flightpath 2050 goals
The main impact and benefits of the proposed project are therefore:
  Efficient and affordable certification of new and innovative safety enhancement systems and operations, with special characteristics that are not yet covered in existing Certification Specifications
  Increase in safety : take ACARE “80% reduction of accident rate by 2020” as safety performance target, and contribute significantly by focusing on novel systems and operations for priority areas that exhibit relatively high risk

## Slide 6: Which EASp operational issues will ASCOS address?
Operational safety issue | Frequency per flight (derived in ASCOS)
Controlled Flight Into Terrain | 3.72∙10 -8
Loss of control in flight | 4.13∙10-7
Ground collision | 1.17∙10-6
Mid-air collision | 3.67∙10-8
Runway excursion | 1.24∙10-6

## Slide 7: Project objectives
To develop certification process adaptations, with supporting tools for safety based design and safety monitoring, so as to ease the introduction and certification of safety enhancements
To achieve this, six measureable and verifiable objectives are defined:
To analyse the existing European certification and rulemaking process and propose potential adaptations to ease certification of safety enhancement systems & operations;
To develop a methodology and supporting tools for multi-stakeholder Continuous Safety Monitoring, using a baseline risk picture for all the parts of the total aviation system;
To develop a total aviation system safety assessment method and supporting tools that can be used for safety based design of new systems, products and/or operations;
To apply proposed certification process adaptations and the design systems and tools in case studies, so as to show how they can be used by operators and manufacturers.
To validate key results: a) new certification approach, b) method and tools for Continuous Safety Monitoring, and c) all the supporting safety based design systems and tools.
To inform air transport stakeholders on the proposed certification approach through promotion workshops, supported by exercises and an e-learning web-site environment.

## Slide 8: Relation between the objectives (and WPs)

## Slide 9: Phase 1 (ongoing)
Analyze existing European certification & rulemaking process and identify potential shortcomings and bottlenecks in view of foreseen regulatory changes & technology developments
Define and evaluate innovative approaches to certification
Further develop proposed certification process adaptations

## Slide 10: Phase 2 (ongoing)
Set up a baseline for the current risk level of the various parts of the total aviation system during its complete life cycle.
Aviation safety data will be used to establish a baseline risk picture for main operational issues identified in the European Aviation Safety Plan (EASP) with Safety Performance Indicators
This risk picture will be used as baseline to set up a process (and develop tools) for continuous safety monitoring

## Slide 11: Phase 3 (ongoing)
Establish a good view on potential emergent and future risks not present in today's aviation system
Develop total aviation system safety assessment method with supporting safety based design systems and tools
Proactive approach to ensure that potential future hazards and risks can be mitigated and safety will be maintained or even increased as compared to the baseline risk picture

## Slide 12: Phase 4 (starting January 2014)
Apply the newly proposed certification process adaptations, and its supporting methods and tools for continuous safety monitoring and safety based design, in four case studies
This is followed by quantification of the safety impact of introduction of new operations and systems in Europe

## Slide 13: Phase 5 (starting January 2014)
The fifth phase validates the scientific and technological advance that the proposed project is expected to bring:
  New affordable certification processes to make certification easier;
  Innovative safety based design systems and tools; and
  New methods and tools to support continuous safety monitoring.

## Slide 14: Contact us http://www.ascos-project.eu
ASCOS coordinator:
  Dr. Ir. Lennaert Speijker
  NLR Air Transport Safety Institute
  Email: speijker@nlr-atsi.nl
  Phone : +31 88 511 3654
Scientific Officer:
  Dr. Michael Kyriakopoulos
  European Commission
  DG Research and Innovation – Aeronautics & Air Transport
  Email: michael.kyriakopoulos@ec.europa.eu

## Slide 15
Aviation Safety and Certification of new Operations and Systems